## Slide 1: Angle Modulation
Prepared by
Rifat Rahman
Assistant Professor
Institute of Appropriate Technology, BUET
https://rrahman007.buet.ac.bd
and
Prof. Hitesh Dholakiya

## Slide 2: Spectral Components of Angle Modulation
Equation of Frequency Modulation {If the carrier signal is 𝐕𝐂 𝐬𝐢𝐧 𝛚𝐜𝐭 and the Message Signal is 𝐕𝐦 𝐜𝐨𝐬 𝛚𝐦𝐭 } is given by:
[Here, Modulation Index,
Here,, ……… are Bessel Function and their value depends on Modulation Index.
)
)
)
) …]

## Slide 3: Bessel Function Table with respect to Modulation Index

## Slide 4: Observation from Bassel Function Table
FM wave consists of the carrier {The first term in the equation}.
FM wave consists of an infinite number of sidebands.
The magnitude 𝐕𝐂𝐉𝐧 of the carrier and sidebands depends on the Bessel Function.
Some Bessel Function can be negative. Therefore, there is a 180 degree phase shift for that given sidebands.
For Certain value of modulation index, the carrier component will disappear completely. These values are called eigen values.
For FM Signal, Transmitted power always remains constant. It is not dependent on modulation index.
𝐕𝐂𝟐
⟹ 𝐏𝐭 = 𝟐𝐑

## Slide 5: Bandwidth of FM wave
Theoretically, the bandwidth of the FM wave is Infinite. But, practically, it is calculated based on how many sidebands have significant amplitude. The Simplest method to calculate the bandwidth is as under:
⟹ 𝐁𝐖 = 𝟐𝐅𝐦 × 𝐍𝐮𝐦𝐛𝐞𝐫 𝐨𝐟 𝐒𝐢𝐠𝐧𝐢𝐟𝐢𝐜𝐚𝐧𝐭 𝐒𝐢𝐝𝐞𝐛𝐚𝐧𝐝𝐬
The second method is based on Carson’s Rule.
It States that the bandwidth of FM Wave is twice the sum of the deviation and highest modulating frequency.
⟹ 𝐁𝐖 = 𝟐 ∆𝐅 + 𝐅𝐦
Carson’s Rule accommodates almost 98% of the Transmitted Power.
Parameters | DSB-FC | DSB-SC | SSB-SC | VSB
Bandwidth | 𝟐𝐅𝐦 | 𝟐𝐅𝐦 | 𝐅𝐦 | 𝐅𝐦 + 𝐅𝐕 25% to 30% greater then SSB.
The Bandwidth of FM is greater than AM, but FM has better noise immunity.

## Slide 6: Example 1. A carrier wave of amplitude 10V and frequency 100 MHz is frequency modulated by a sinusoidal voltage. The modulating voltage has an amplitude of 5V and a frequency 𝐟𝐦 = 𝟐𝟎 𝐤𝐇𝐳. The frequency deviation constant is 2 kHz/Volt. Draw the frequency spectrum of FM wave.

## Slide 8: Bassel Function Table with respect to Modulation Index

## Slide 9: Narrow Band Frequency Modulation (NBFM)
Outlines
Basics of NBFM
Derivation of the Equation of NBFM
Essential Keynotes of NBFM
NBFM Generation
Resolution of Issue in NBFM Generation

## Slide 10: Basics of NBFM
NBFM is used to improve spectrum efficiency {Narrow Bandwidth}.
NBFM is used in Voice Communication and Radio Settings.
Modulation Index for NBFM is less than 1.
and the Message
Equation of Frequency Modulation {If the carrier signal is 𝐕𝐂 𝐜𝐨𝐬 𝛚𝐜𝐭
Signal is 𝐕𝐦 𝐜𝐨𝐬 𝛚𝐦𝐭 } is given by:
For Small values of Modulation Index, 𝐜𝐨𝐬 𝐦𝐟 𝐬𝐢𝐧 𝛚𝐦𝐭
= 𝟏, 𝐬𝐢𝐧 𝐦𝐟 𝐬𝐢𝐧 𝛚𝐦𝐭
= 𝐦𝐟 𝐬𝐢𝐧 𝛚𝐦𝐭
𝐟
∆𝐅
Here, Modulation Index 𝐦 =
𝐅𝐦
Derivation of the Equation of NBFM
⟹ 𝐘𝐅𝐌 𝐭 = 𝐕 𝐜𝐨𝐬
𝐂 𝐜
𝛚 𝐭 +
𝐤 𝐕
𝐟 𝐦
𝐅𝐦
𝐦
𝐬𝐢𝐧 𝛚 𝐭
⟹ 𝐘𝐅𝐌
⟹ 𝐘𝐅𝐌
𝐭 = 𝐕𝐂 𝐜𝐨𝐬 𝛚𝐜𝐭 + 𝐦𝐟 𝐬𝐢𝐧 𝛚𝐦𝐭
𝐭 = 𝐕𝐂 𝐜𝐨𝐬 𝛚𝐜𝐭 𝐜𝐨𝐬 𝐦𝐟 𝐬𝐢𝐧 𝛚𝐦𝐭
− 𝐬𝐢𝐧 𝛚𝐜𝐭 𝐬𝐢𝐧 𝐦𝐟 𝐬𝐢𝐧 𝛚𝐦𝐭
⟹ 𝐘𝐅𝐌
⟹ 𝐘𝐅𝐌
𝐭 = 𝐕𝐂 𝐜𝐨𝐬 𝛚𝐜𝐭 − 𝐦𝐟 𝐬𝐢𝐧 𝛚𝐜𝐭 𝐬𝐢𝐧 𝛚𝐦𝐭
𝐭 = 𝐕𝐂 𝐜𝐨𝐬 𝛚𝐜𝐭 − 𝐕𝐂𝐦𝐟 𝐬𝐢𝐧 𝛚𝐜𝐭 𝐬𝐢𝐧 𝛚𝐦𝐭
⟹ 𝐘
𝐅𝐌
𝐭 = 𝐕𝐂 𝐜𝐨𝐬 𝛚𝐜𝐭 +
𝐕 𝐦
𝐂 𝐟
𝟐
𝐜
𝐜𝐨𝐬 𝛚 𝐭 + 𝛚
𝐦
𝐭 −
𝐕 𝐦
𝐂 𝐟
𝟐
𝐜
𝐦
𝐜𝐨𝐬 𝛚 𝐭 − 𝛚 𝐭
Carrier
USB
LSB

## Slide 11: Essential Keynotes of NBFM
and the Message Signal is
Equation of NBFM {If the carrier signal is 𝐕𝐂 𝐜𝐨𝐬 𝛚𝐜𝐭
𝐕𝐦 𝐜𝐨𝐬 𝛚𝐦𝐭 } is given by:
𝐂 𝐜
⟹ 𝐘𝐅𝐌 𝐭 = 𝐕 𝐜𝐨𝐬 𝛚 𝐭
+
𝐂 𝐟
𝟐
𝐜𝐨𝐬 𝛚 𝐭 + 𝛚
𝐜 𝐦
𝐭 −
𝐕 𝐦 𝐕 𝐦
𝐂 𝐟
𝟐
𝐜
𝐦
𝐜𝐨𝐬 𝛚 𝐭 − 𝛚 𝐭
LSB
⟹ 𝐘𝐅𝐌
⟹ 𝐘𝐅𝐌
Carrier
𝐭 = 𝐕𝐂 𝐜𝐨𝐬 𝛚𝐜𝐭
𝐭 = 𝐕𝐂 𝐜𝐨𝐬 𝛚𝐜𝐭
USB
− 𝐕𝐂𝐦𝐟 𝐬𝐢𝐧 𝛚𝐜𝐭 𝐬𝐢𝐧 𝛚𝐦𝐭
− 𝐕𝐂𝐤𝐟𝐠 𝐭 𝐬𝐢𝐧 𝛚𝐜𝐭
LSB is 𝟏𝟖𝟎𝟎 out of phase with respect to USB.
Modulation Index is less then 1 𝐦𝐟 < 𝟏 .
NBFM has only two side bands.
𝐕𝐂𝐦𝐟
Amplitude of the sidebands is .
𝟐
Frequency Deviation ΔF is limited in NBFM.
Modulation Index 𝐦
𝐟
= 𝐤𝐟𝐕𝐦 = ∆𝐅
𝐅𝐦 𝐅𝐦
Here,

## Slide 12: NBFM Generation
and the Message Signal is
Equation of NBFM {If the carrier signal is 𝐕𝐂 𝐜𝐨𝐬 𝛚𝐜𝐭
𝐕𝐦 𝐜𝐨𝐬 𝛚𝐦𝐭 } is given by:
⟹ 𝐘𝐅𝐌 𝐭 =
𝐕𝐂 𝐜𝐨𝐬 𝛚𝐜𝐭
Carrier
− 𝐕𝐂𝐤𝐟𝐠 𝐭 𝐬𝐢𝐧 𝛚𝐜𝐭 Here, 𝐠 𝐭 = න 𝐦 𝐭 𝐝𝐭
Sidebands
𝐦 𝐭 Modulating Signal
Integrator
t
න 𝐦 𝐭 𝐝𝐭
Carrier Oscillator
𝐕𝐂 𝐜𝐨𝐬 𝛚𝐜𝐭
𝛑/𝟐
Phase
−𝐕𝐂 𝐬𝐢𝐧 𝛚𝐜𝐭
DSB-SC Modulator
−𝐕𝐂𝐤𝐟𝐠 𝐭 𝐬𝐢𝐧 𝛚𝐜𝐭
Adder
NBFM Signal
Here,

## Slide 13: Resolution of Issue in NBFM Generation
Amplitude variation can occur due to the adder. A Bandpass Limiter can resolve that issue.
NBFM Signal
Hard Limiter
BPF
Pure NBFM Signal
Hard Limiter converts NBFM Signal into a Square wave.
The output of the Hard Limiter is given by:
⟹ 𝐘′ 𝐭 = ቊ
+𝟏 𝐜𝐨𝐬 𝛉 > 0
−𝟏 𝐜𝐨𝐬 𝛉 < 0
⟹ 𝐘′ 𝐭 =
𝟒
𝛑
𝟏
𝟑
𝟏
𝟓
𝐜𝐨𝐬 𝛉 − 𝐜𝐨𝐬 𝟑𝛉 + 𝐜𝐨𝐬 𝟓𝛉 − … … …
BPF will allow only 𝐜𝐨𝐬 𝛉 component.
So, Pure NBFM Signal will be given by:
𝟒
⟹ 𝐘𝐅𝐌 𝐭 = 𝛑 𝐜𝐨𝐬 𝛉
𝐖𝐡𝐞𝐫𝐞, ⟹ 𝛉 = 𝛚𝐜𝐭 + 𝟐𝛑𝐤𝐅 න 𝐦 𝐭 𝐝𝐭

## Slide 14: + 𝟎. 𝟓 𝐜𝐨𝐬 𝛚𝐦𝐭 𝐬𝐢𝐧 𝛚𝐜𝐭 is ………………..
Example 2. The Signal 𝐜𝐨𝐬 𝛚𝐜𝐭
FM only
AM only
Both AM and FM
Neither AM nor FM

## Slide 15: Narrow Band Phase Modulation (NBPM)
Outlines
Basics of NBPM
Equation of NBPM
NBPM Generation
Resolution of Issue in NBPM Generation

## Slide 16: Basics of NBPM
NBPM is used to improve spectrum efficiency {Narrow Bandwidth} {It is similar to NBFM}.
Modulation Index for NBPM is less than 1.
and the
Equation of Phase Modulation {If the carrier signal is 𝐂 𝐭 = 𝐕𝐂 𝐜𝐨𝐬 𝛚𝐜𝐭
Message Signal is 𝐦 𝐭 = 𝐕𝐦 𝐜𝐨𝐬 𝛚𝐦𝐭 } is given by:
= 𝟏, 𝐬𝐢𝐧 𝐦𝐏 𝐜𝐨𝐬 𝛚𝐦𝐭
= 𝐦𝐏 𝐜𝐨𝐬 𝛚𝐦𝐭
Here, Modulation Index 𝐦𝐏 = 𝐤𝐏𝐕𝐦
Derivation of the Equation of NBPM
⟹ 𝐘𝐏𝐌
⟹ 𝐘𝐏𝐌
⟹ 𝐘𝐏𝐌
𝐭 = 𝐕𝐂 𝐜𝐨𝐬 𝛚𝐜𝐭 + 𝐤𝐏𝐦 𝐭
𝐭 = 𝐕𝐂 𝐜𝐨𝐬 𝛚𝐜𝐭 + 𝐦𝐏 𝐜𝐨𝐬 𝛚𝐦𝐭
𝐭 = 𝐕𝐂 𝐜𝐨𝐬 𝛚𝐜𝐭 𝐜𝐨𝐬 𝐦𝐏 𝐜𝐨𝐬 𝛚𝐦𝐭
− 𝐬𝐢𝐧 𝛚𝐜𝐭 𝐬𝐢𝐧 𝐦𝐏 𝐜𝐨𝐬 𝛚𝐦𝐭
For Small values of Modulation Index, 𝐜𝐨𝐬 𝐦𝐏 𝐜𝐨𝐬 𝛚𝐦𝐭
⟹ 𝐘𝐏𝐌 𝐭 = 𝐕𝐂 𝐜𝐨𝐬 𝛚𝐜𝐭 − 𝐦𝐏 𝐬𝐢𝐧 𝛚𝐜𝐭 𝐜𝐨𝐬 𝛚𝐦𝐭
Carrier
Sidebands
⟹ 𝐘𝐏𝐌 𝐭 =
𝐕𝐂 𝐜𝐨𝐬 𝛚𝐜𝐭
−
𝐕𝐂𝐤𝐏𝐦 𝐭 𝐬𝐢𝐧 𝛚𝐜𝐭

## Slide 17: NBPM Generation
and the Message Signal is
Equation of NBPM {If the carrier signal is 𝐕𝐂 𝐜𝐨𝐬 𝛚𝐜𝐭
𝐕𝐦 𝐜𝐨𝐬 𝛚𝐦𝐭 } is given by:
Carrier
⟹ 𝐘𝐏𝐌 𝐭 =
𝐕𝐂 𝐜𝐨𝐬 𝛚𝐜𝐭
−
𝐕𝐂𝐤𝐏𝐦 𝐭 𝐬𝐢𝐧 𝛚𝐜𝐭
𝐦 𝐭 Modulating Signal
Carrier
Oscillator
𝐕𝐂 𝐜𝐨𝐬 𝛚𝐜𝐭
𝛑/𝟐
Phase
−𝐕𝐂 𝐬𝐢𝐧 𝛚𝐜𝐭
DSB-SC Modulator
Sidebands
−𝐕𝐂𝐤𝐩𝐦 𝐭 𝐬𝐢𝐧 𝛚𝐜𝐭
Adder
NBPM Signal

## Slide 18: Resolution of Issue in NBPM Generation
Amplitude variation can occur due to the adder. A Bandpass Limiter can resolve that issue.
NBPM Signal
Hard Limiter
BPF
Pure NBPM Signal
Hard Limiter converts NBPM Signal into a Square wave.
The output of the Hard Limiter is given by:
⟹ 𝐘′ 𝐭 = ቊ
+𝟏 𝐜𝐨𝐬 𝛉 > 0
−𝟏 𝐜𝐨𝐬 𝛉 < 0
𝟒 𝟏 𝟏
⟹ 𝐘′ 𝐭 = 𝛑 𝐜𝐨𝐬 𝛉 − 𝟑 𝐜𝐨𝐬 𝟑𝛉 + 𝟓 𝐜𝐨𝐬 𝟓𝛉 − … … …
BPF will allow only 𝐜𝐨𝐬 𝛉 component.
So, Pure NBPM Signal will be given by:
𝟒
⟹ 𝐘𝐏𝐌 𝐭 = 𝛑 𝐜𝐨𝐬 𝛉
𝐖𝐡𝐞𝐫𝐞, ⟹ 𝛉 = 𝛚𝐜𝐭 + 𝐤𝐏𝐦 𝐭

## Slide 19: Wide Band Frequency Modulation (WBFM)
Outlines
Basics of WBFM
Bessel Function Table with respect to Modulation Index
WBFM Generation
Applications of WBFM

## Slide 20: Basics of WBFM
Modulation Index 𝐦𝐟 for WBFM is Greater than 1.
and the Message
The bandwidth of WBFM is several times the message Bandwidth.
Equation of Frequency Modulation {If the carrier signal is 𝐕𝐂 𝐬𝐢𝐧 𝛚𝐜𝐭
Signal is 𝐕𝐦 𝐜𝐨𝐬 𝛚𝐦𝐭 } is given by:
In WBFM, as Modulation Index is greater then 1, Bassel Function 𝐉𝐧 has more elements.
𝐟
Here, Modulation Index 𝐦 =
∆𝐅
𝐅
𝐦
)
)
)
) …
[Here, Modulation Index,

## Slide 21: Bassel Function Table with respect to Modulation Index

## Slide 22: WBFM Generation
1. Direct Method
𝐦 𝐭 Modulating Signal
VCO
WBFM
Signal
VCO Produce Output whose frequency is proportional to input message signal 𝐦 𝐭 .
⟹ 𝐟𝐨 = 𝐟𝐜 + 𝐤𝐅𝐦 𝐭
2. Indirect Method
NBFM
Modulator
Frequency Multiplier
WBFM
Signal
𝐦 𝐭 Modulating Signal
NBFM
Signal
𝐕𝐂 𝐜𝐨𝐬 𝛚𝐜𝐭
Frequency Multiplier produces signal whose frequency is n times of input frequency.

## Slide 23: Applications of WBFM
WBFM is widely used in FM Radio Broadcast {88 MHz to 108 MHz}.
  FM Frequency Deviation is 75 KHz, for a 15 kHz Audio Band, there are 5 Bands.
WBFM is used in a High-Fidelity Audio System.
WBFM is used in Satellite Communication.
WBFM is also used in Telemetry, which has a large data range.

## Slide 24: FM Generation by Direct Method
Basics of FM Signal
In Frequency Modulation, the Frequency of the Carrier Signal changes with respect to the Modulating Signal.
  Let the Carrier Signal is given by:  Then, the Frequency Modulated Signal is given by:
⟹ 𝐂 𝐭 = 𝐕𝐂 𝐜𝐨𝐬 𝛚𝐜𝐭 ⟹ 𝐘𝐅𝐌 𝐭 = 𝐕𝐂 𝐜𝐨𝐬 𝛚 𝐭 𝐭 = 𝐕𝐂 𝐜𝐨𝐬 𝛉 𝐭
    Here, 𝛚 𝐭 and 𝛉 𝐭 is a function of the Message Signal 𝐦 𝐭 .
Frequency Modulation is a part of the Angle Modulation, The Angle of Frequency
Modulation is given by:
𝛚𝐜𝐭 +
The Frequency is given by:
⟹ 𝛚 𝐭 = 𝛚𝐜 +
𝐤𝐅 is frequency Sensitivity, Unit is Hz/Volt.

## Slide 25: Direct Method for FM Generation
𝐂𝟎
𝐋
Message Signal
𝐦 𝐭
Variable Reactor
P
Depletion
Region
N
Using Voltage Controlled Oscillator (VCO), The frequency of Carrier signal can be
controlled by an external voltage (Message Signal).
  Heartily or Colpitts Oscillator
  Schmitt Trigger Circuit
  Saturable Core Reactor
d
𝐀
⟹ 𝐂′ = 𝛆𝟎𝛆𝐫 𝐝
⟹ 𝐂′ = −𝐤𝐦 𝐭
Effective Capacitance:
⟹ 𝐂 = 𝐂𝟎 + 𝐂′ = 𝐂𝟎 − 𝐤𝐦 𝐭
Tank Circuit

## Slide 26: Derivation of FM Signal using Direct Method for FM Generation
Higher orders of the Taylor’s series will be neglected

## Slide 27
Advantages of Direct Method for FM Generation
It generates sufficient frequency deviation.
It requires little frequency multiplication.
Disadvantages of Direct Method for FM Generation
It has Poor Frequency Stability.

## Slide 28: FM Generation by Indirect Method of Armstrong Block Diagram of FM Generation by Indirect Method of Armstrong
𝐦 𝐭 Modulating Signal
NBFM
Frequency Multiplier
Frequency Conversion
Frequency Multiplier
FM
Signal
Crystal
Oscillator

## Slide 29: NBFM Generation
and the Message Signal is
Equation of NBFM {If the carrier signal is 𝐕𝐂 𝐜𝐨𝐬 𝛚𝐜𝐭
𝐕𝐦 𝐜𝐨𝐬 𝛚𝐦𝐭 } is given by:
⟹ 𝐘𝐅𝐌 𝐭 =
𝐕𝐂 𝐜𝐨𝐬 𝛚𝐜𝐭
Carrier
− 𝐕𝐂𝐤𝐟𝐠 𝐭 𝐬𝐢𝐧 𝛚𝐜𝐭 Here, 𝐠 𝐭 = න 𝐦 𝐭 𝐝𝐭
Sidebands
𝐦 𝐭 Modulating Signal
Integrator
t
න 𝐦 𝐭 𝐝𝐭
Carrier Oscillator
𝐕𝐂 𝐜𝐨𝐬 𝛚𝐜𝐭
𝛑/𝟐
Phase
−𝐕𝐂 𝐬𝐢𝐧 𝛚𝐜𝐭
DSB-SC Modulator
−𝐕𝐂𝐤𝐟𝐠 𝐭 𝐬𝐢𝐧 𝛚𝐜𝐭
Adder
NBFM Signal
Here,

## Slide 30
Frequency Multiplier
NLD
BPF

## Slide 31: FM Demodulation
Outlines
FM Demodulation using Envelope Detector
Waveforms of FM Demodulation using Envelope Detector

## Slide 32: FM Demodulation using Envelope Detector
Differentiator
Envelope
Detector
HPF

## Slide 33: Circuit Diagram
Differentiator
Envelope
Detector
HPF
𝐘𝐅𝐌
𝐭
𝛟F𝐌
𝐭
𝐘𝐄𝐃
𝐭
𝐦 𝐭
The Transfer Function of Differentiator 𝐇 𝐟 is directly Propositional to Frequency F.
⟹ 𝐇 𝐟 ∝ 𝐟
The Differentiator could be designed using High Pass Filter HPF.
𝐂
𝐑
𝛟F𝐌
𝐭
𝐘𝐅𝐌
𝐭
𝛟𝐅𝐌
⟹ 𝐇 𝐟 =
𝐘F𝐌
𝐑 + 𝟏
𝐣𝛚𝐂
= =
𝐟 𝐑 𝐣𝛚𝐂𝐑
𝐟 𝟏 + 𝐣𝛚𝐂𝐑
The Transfer Function is given by:
If 𝛚𝐑𝐂 ≪ 𝟏, then
⟹ 𝐇 𝐟 = 𝐣𝛚𝐂𝐑
⟹ 𝐇 𝐟 ∝ 𝐟
𝐝𝐭
Here, The differentiator 𝐝𝐘𝐅𝐌 = Slope

## Slide 34: Waveforms of FM Demodulation using Envelope Detector
Time t (Sec)
Amplitude Message Signal 𝐱 𝐭
Time t (Sec)
Amplitude
FM Signal 𝐘𝐅𝐌 𝐭
𝐕𝐂
−𝐕𝐂
⟹ 𝐘𝐅𝐌
𝐭 = 𝐕𝐂 𝐜𝐨𝐬
𝒕
𝛚𝐜𝐭 + 𝟐𝛑𝐤𝐅 න 𝐦 𝐭 𝐝𝐭
𝟎
Time t (Sec)
Amplitude
Envelope Signal 𝐲′ 𝐭

## Slide 35: FM Demodulation by Phase Lock Loop
Block Diagram of Phase Lock Loop
Loop Filter
VCO
FM wave
𝐒 𝐭
𝐫 𝐭
𝐞 𝐭
𝐯 𝐭
The Phase Lock Loop has three essential elements with Negative feedback:
  Multiplier: It is used as a Phase Detector.
  VCO: It works as a Local Oscillator.
  Loop Filter: It acts as a Low Pass Filter.

## Slide 37: Linear Model of Phase Lock Loop
𝚽𝟏 𝐭
𝚽𝟐 𝐭
𝚽𝐞 𝐭
𝐯 𝐭
∑
_
𝐭
න 𝐝𝐭
𝟎
𝐡 𝐭
𝟐𝛑𝐤𝟎
𝟏/𝟐𝛑𝐤𝐕